## Slide 1: Communication Workflow — MQTT Design & Handshakes
عهدنامه و پیمان اخوت برای ارتباطات بین ماژول و سرور
15/5/1404

## Slide 2
SIM7000
SIM800
GPS
RFID
RTC
Stepper
Gyroscope

## Slide 3: Topic structures QoS & Reliability Configurations

## Slide 4: MQTT QoS & Reliability Configurations
Feature | Choice | Reason
QoS Level | QoS 1 | Ensures delivery even with intermittent connectivity. Lightweight compared to QoS 2.
*Last Will and Testament (LWT) | No | We cannot implement it with SIM800 module
*Persistent Sessions | No | Not needed
Retained Messages | Yes on some topics | Use retained messages for static config data (e.g., latest unlock command) but NOT for status updates.
Session Expiry Interval | Set to few minutes (e.g., 5 minutes) | Gives time to reconnect and receive pending commands. Prevents broker from holding stale sessions indefinitely.

## Slide 5
MQTT QoS & Reliability Configurations
QoS
1
At least once - Guaranteed delivery, but can be delivered more than once.
Needs ACK.
MQTT Client
MQTT Broker
Publish QoS 1
PUBACK

## Slide 6: Topics Structure
status
→ Publishes GPS, timestamp, and battery level data.
→ Receives lock/unlock commands from the backend.
→ Publishes scanned RFID tag IDs for authorization requests.
→ Receives configuration updates (gyroscope).
truck
<IMEI>
rfid
command
lock
config
gyroscope
rfid
wit
→ Receives configuration updates (RFID).
→ Receives configuration updates (wake-up interval).
sms
gyroscope
→ Publishes the phone number and the lock command that it sends.
→ Publishes the sudden erupts or movements of the device
Fleet
Fleet ID

## Slide 7: Topics Structure
Topic Type | Topic address | Notes
Status Data | truck/<IMEI>/status | Publishes timestamp, GPS data, battery level, Lock status, Temperature, RSSI, Counter and isQueued to server
RFID Scan | truck/<IMEI>/rfid | Publishes scanned timestamp, GPS, RFID tag serial number and requested action to server.
SMS Alarm | truck/<IMEI>/sms | When a user sends SMS to lock/unlock the device, a msg publishes on this topic to alert the web app
Gyroscope Alarm | truck/<IMEI>/gyroscope | When the device detects a sudden movement greater that the configured threshold, publishes alarm to the web app on this topic
Command Control - lock | truck/<IMEI>/command/lock | Server publishes unlock/lock commands here.
Command Control – Gyro config | truck/<IMEI>/command/config/gyroscope | Server publishes configuration commands for Gyroscope
Command Control – Gyro config | truck/<IMEI>/command/config/rfid | Server publishes configuration commands for RFID
Command Control – Gyro config | truck/<IMEI>/command/config/wit | Server publishes configuration commands to determine the wake-up interval.

## Slide 8: Msg structures
Status, Command, RFID, LWT

## Slide 9: Status Payload format
Truck
<IMEI>
Status
{
"time": “hour,minute,seccond",
"lat": 52.520008,
"lon": 13.404954,
“gps source”: G/B which determines if the data comes from device gps or the nearest BTS
“GPS distances traveled”: a float with one floating point digit in kilometers
“total traveled”: an int to show total traveled distance in meters
“Speed”: the speed that comes from gps, a float number with two floating point number
"battery " : 0-9, // 9 -> means 90% to 100%, 5 means 50% to 60%
" lock status" : L/U //lock/unlock
" temperature " : 27 //temperature based on Celsius
"rssi": -78, // optional but useful for diagnostics
" counter": 7 // the Nth transmission
" is queued ": 0/1 // is msg queued or not
“is in geo-fence” Y/N determines if the device is in geo-fence or not
“distance from geo-fence”: distance in meter from geo-fence
}
HH | MM | SS | Lat | Lon | GPS source | TraveledDist | totalTraveledDist | speed | Batt | Lock | Temp | RSSI | Cnt | Queued | isInGeo | distanceToGeo
05 | 20 | 15 | 52.520008 | 13.40495 | G/B | 5.2 | 6.3 | 60.72 | 8 | L/U | 27 | 25 | 100 | 0/1 | Y/N | 50000

## Slide 10
Truck
<IMEI>
RFID
{
"rfid": "E2003412010901123456789A",
“action request": L/U/N //indicates lock/unlock/Not registered
}
Example messages :
“{E2003412010901123456789A, U}”
Command , RFID Scan and LWT Payload
“{E2003412010901123456789A, L}”
“{E2003412010901123456789A, N}”

## Slide 11
Truck
<IMEI>
SMS
{
“phone number": “0912*********",
“action": L/U //indicates lock/unlock
}
Example messages :
“{09126891656, U}”
Command , RFID Scan and LWT Payload
“{09126891656, L}”

## Slide 12
Truck
<IMEI>
gyroscope
{
"": "",
“request":
}
Example messages :
“{E2003412010901123456789A, U}”
Command , RFID Scan and LWT Payload
“{E2003412010901123456789A, L}”
“{E2003412010901123456789A, N}”

## Slide 13
Truck
<IMEI>
Command
{
“command”: lock_open/lock_close
}
Lock
“{lock_open}”
“{lock_close}”
Lock Command Message Structure

## Slide 14
Truck
<IMEI>
Command
gyroscope
config
“{gyro_off}”
Config Command Message Structure
rfid
wit
{
ON/OFF
}
{
ON/OFF
}
{
#second // indicates Wake-up Interval Time
}
“{gyro_on_1}”
“{off}”
“{on}”
“{wit_on_60}”
“{wit_off}”
“{wit_on_240}”

## Slide 15: Timing intervals
GPS and network timings

## Slide 16
Timing and samplings
X seconds intervals GPS sampling
Y seconds intervals, Network connection
#1 No network failure
Queue log, set the next network retry
Reconnection Successful.
Send all queued msgs
Queue status, no connection tryout
#2 No network failure
Queue log, set the next network retry
Queue status, no connection tryout
Queue status, no connection tryout
Queue status, no connection tryout
Sampling interval
GPS
Network
Conn.
Wait for WIT * 2
Wait for WIT * 2