## Slide 1: Test Module NodeMCU Code
Network setup, topics, broker connection

## Slide 2
NodeMCU V2.0 Pinout

## Slide 3: Network Setup
Check the Wi-Fi configs in code. Enter the correct ssid (network name) and password.
Check the MQTT Setting configs in code. Enter the correct broker Public IP address in mqtt_server.
If the above settings are correct, after uploading the code into the board and opening serial monitor (in 155200 baud) you should see success output like below.

## Slide 4: Board
Four LEDs are used in this test module
Green: ON Wi-Fi is connected/ OFF Wi-Fi is not connected
Red: ON Wi-Fi has disconnected
Blue: Module Has sent a payload through MQTT
Yellow: Module Has received a payload from MQTT
At the beginning of the process all four LEDs will be On for 1 seconds.

## Slide 5: Topics
Publishes on: test/truck/0/data
Can send any payload
Subscribes to: test/truck/0/command/lock
Expect to receive ‘lock’ and ‘unlock’ text payloads.
Rotates the servo motor accordingly.
mosquitto_sub -h 2.177.238.83 -t test/truck/0/data
Test Module NodeMCU
Broker
mosquitto_pub -h 2.177.238.83 -p 1883 -t "test/truck/0/command/lock" -m "lock"